## Slide 1: The Memory Hierarchy
① Storage Technologies and Trends
② Locality of Reference
③ Caching in the Memory Hierarchy
Understand Storage Technologies and Trends
Identify
Locality in a Program
Understand Caching in the Memory Hierarchy

## Slide 2: Random-access Memory (RAM)
 | Trans /bit | Access time | Needs refresh | Cost | Applications
SRAM | 4 or 6 | 1x | No | 100x | Cache memories
DRAM | 1 | 10x | Yes | 1x | Main memories
Notes: RAM is traditionally packaged as a chip.
Basic storage unit is normally a cell (one bit per cell).
Multiple RAM chips form a memory.
SRAM (Static RAM)
DRAM (Dynamic RAM)

## Slide 3: Dynamic RAM
Word Line
Bit Line

## Slide 4: Static RAM
Word Line
Bit Line
~Bit Line

## Slide 5: Nonvolatile Memories
Read-only memory (ROM)
Programmable ROM (PROM)
Erasable PROM (EPROM)
Electrically erasable PROM (EEPROM)
Flash memory
Notes: Read-only memory (ROM): programmed during production
Programmable ROM (PROM): can be programmed once
Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
Electrically eraseable PROM (EEPROM): electronic erase capability
Flash memory: EEPROMs. with partial (block-level) erase capability
Wears out after about 100,000 erasings
Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
Disk caches

## Slide 6: Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Notes: A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Load operation
Store operation

## Slide 7: Rotating Disk
Arm
Platters
Spindle

## Slide 8: Disk Access
Track/Cylinder

## Slide 9: Reading a Disk Sector
Main
memory
I/O
bridge
Bus interface
ALU
Register file
Disk
controller
Graphics
adapter
USB
controller
mouse/keyboard
Monitor
I/O bus
Disk

## Slide 10: Solid State Disks
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Notes: Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after about 100,000 repeated writes.
Advantages
No moving parts  faster, less power, more rugged
Disadvantages
Have the potential to wear out
Mitigated by “wear leveling logic” in flash translation layer
E.g. Intel SSD 730 guarantees 128 petabyte (128 x 1015 bytes) of writes before they wear out
In 2015, about 30 times more expensive per byte
Applications
MP3 players, smart phones, laptops
Beginning to appear in desktops and servers

## Slide 12: The CPU-Memory Gap
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08

## Slide 13: Locality
Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality
Spatial locality

## Slide 14: Locality Example
Temporal locality
Spatial locality
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;

## Slide 15
Q: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 16
Q: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 17
Q: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 18: Fundamental properties
Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
The gap between CPU and main memory speed is widening.
Well-written programs tend to exhibit good locality.

## Slide 19
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
Remote secondary storage
(distributed file systems, Web servers)
L2 cache
(SRAM)
Smaller,
Faster,
costlier
L3 cache
(SRAM)
Notes: Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 20: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Slower memory viewed as
partitioned into “blocks”
Data is copied in
block-sized transfer units
Faster memory caches a subset of the blocks
4
4
4
10
10
10

## Slide 21: Cache Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 22: Cache Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12

## Slide 23
Cache Type | What is Cached? | Where is it Cached? | Latency (cycles) | Managed by
Registers | 4-8 bytes words | CPU core | 0 | Compiler
TLB | Address translations | On-chip TLB | 0 | Hardware MMU
L1 cache | 64-byte blocks | On-Chip L1 | 4 | Hardware
L2 cache | 64-byte blocks | On-Chip L2 | 10 | Hardware
Virtual Memory | 4-KB pages | Main memory | 100 | Hardware + OS
Buffer cache | Parts of files | Main memory | 100 | OS
Disk cache | Disk sectors | Disk controller | 100K | Disk firmware
Network buffer cache | Parts of files | Local disk | 10M | NFS client
Browser cache | Web pages | Local disk | 10M | Web browser
Web cache | Web pages | Remote server disks | 1B | Web proxy server

## Slide 24: Summary
Storage Technologies
  RAM, ROM
  Rotating disk, Solid state disk
Locality
  Temporal
  Spatial
Memory Hierarchy
Cache
  Hit
  Miss

## Slide 25
No one will need more than 637Kb of memory for a personal computer.
Bill Gates
Co-founder of Microsoft